## Slide 1
BTP: EMI Effects in Voltage-to-Time Converters
Analysis, Cadence exploration, and differential EMI-cancellation architecture
G. Jaidev | 2023EEB1200
Guide: Prof. Devarshi Mrinal Das
Department of Electrical Engineering, IIT Ropar

## Slide 2
Project Story: From VTC to EMI-Robust Architecture
Before mid-semester: common VCDU/VTC foundation, PVT study, Monte Carlo and EMI base-paper analysis.
After mid-semester: BTP diverged toward EMI reduction using differential delay architectures.
Main research question: how can common-mode EMI be reduced after voltage is converted to time?
Final direction: compressed small-signal differential control around 0.9 V.
Baseline VTC from literature: two VCDU paths generate a time difference.

## Slide 3
Pre-Midsemester Foundation
VCDU/VTC operation, PVT variation, and baseline EMI susceptibility

## Slide 4
Baseline VCDU/VTC Principle
A VCDU delays an input edge according to a control voltage.
Two VCDUs form a VTC: one input-controlled path and one reference path.
Output is measured as a time difference, not an absolute voltage.
This structure is useful for TMSP but still sensitive to timing disturbances.
Pre-midsem baseline VTC architecture.

## Slide 5
Delay Model Used Throughout BTP
Delay is the capacitor discharge time until the inverter threshold is crossed.
Any perturbation in current or threshold appears as timing jitter.
I_dis = - C_L dV_C/dt
t_d = C_L Delta V / I_ctrl
Delta I ~= g_m Delta V_ctrl
Delta t_d ~= -(C_L Delta V / I_0^2) Delta I

## Slide 6
PVT and Monte Carlo: Single VCDU Sensitivity
Single VCDU delay varies strongly with process, voltage, temperature and mismatch; this was established in the mid-semester work.
Monte Carlo distribution / delay spread
Cadence summary table

## Slide 7
Why Dual VCDU Helps With PVT
Single VCDU: absolute delay includes PVT shift.
Dual VCDU/VTC: output is a difference of two similar paths.
Common PVT delay shifts cancel approximately in Delta T.
This improves timing stability, but does not cancel unequal EMI coupling.
Mid-sem insight: common PVT variation reduces in dual VCDU/VTC.

## Slide 8
Baseline EMI Injection: Core Observation
EMI was modelled as a sinusoidal disturbance. Amplitude, phase and frequency all affect delay.
EMI injected at V_in
All-pin EMI scenario

## Slide 9
Why EMI Phase Matters
A VTC makes a timing decision at one instant. The EMI value at that instant determines edge advance/delay.
v_emi(t)=A_emi sin(2*pi*f_emi*t + phi)
v_emi(t_s)=A_emi sin(2*pi*f_emi*t_s + phi)
Delta t_d proportional to v_emi(t_s)
Worst-case: max_phi |Delta t_d(phi)|

## Slide 10
Baseline VTC Frequency/Phase Sweep
These results motivated the BTP: average delay is not enough; worst-case phase at GHz frequency can be much larger.
Average delay increases with frequency
Delay depends on phase and frequency
Worst-case phase peak at high frequency

## Slide 11
Post-Midsemester Circuit Exploration
Differential delay cells tried after the scope diverged from DEP

## Slide 12
Differential Delay-Cell Literature Survey
Three topologies were reviewed and implemented/analyzed as candidates before choosing the final direction.
Basic differential delay cell
SET-hardened complementary differential cell
Input-conditioned / dual-path delay cell

## Slide 13
Why Basic Differential Delay Was the Starting Point
Differential signalling can reject common-mode noise in principle.
If both branches receive the same EMI, subtraction cancels it.
But the delay cell must still give clean, monotonic voltage-to-time conversion.
This became the selection criterion for later attempts.
Basic differential delay concept.

## Slide 14
SET-Hardened CDC Implementation
This cell was studied because its cross-coupled feedback gives strong switching and robustness.
Internal Cadence schematic
Testbench
Measured delay response

## Slide 15
SET-H CDC: Insight and Limitation
Good for robust/latch-like switching, not automatically good for VTC conversion.
Delay tuning was weak/nonlinear over the input sweep.
Cross-coupled feedback caused abrupt transition behaviour.
Decision: used as design-learning block, not final architecture.
Delay response was not smooth enough for final VTC.

## Slide 16
Input-Conditioned Delay Cell Implementation
This cell was a separate and important attempt; it was not the same as the SET-H CDC.
Internal schematic
Testbench
Differential transient
Delay response

## Slide 17
Input-Conditioned Cell: Why Rejected
Auxiliary control paths made biasing difficult.
Transient output had overshoot/settling and limited clean swing.
Delay extraction became threshold-dependent.
Decision: not suitable as the main VTC delay core.
Irregular delay response under sweep.

## Slide 18
Custom Differential Attempts
What was built in Cadence and why some versions were rejected

## Slide 19
Direct Differential-Pair Controlled Delay Cell
First custom attempt: use a differential pair output to control the differential delay current.
Conceptual differential delay architecture
Expanded schematic
Cadence testbench

## Slide 20
Core Problem: Differential Input Became Single-Ended Control
The front-end was differential, but later the control was effectively single-ended.
Common-mode/supply disturbance re-entered the control current.
Rising and falling delays became unbalanced.
This explained why differential structure alone was not enough.
Rising/falling delay mismatch.

## Slide 21
Direct Attempt: Waveforms and Delay Issues
These figures are kept because they explain the actual design challenge, not as final success claims.
Differential transient output
Two-path VTC testbench
Delay curve
Edge mismatch

## Slide 22
EMI Analysis of Intermediate Architecture
Systematic sweeps across amplitude, phase, control voltage and injection ports

## Slide 23
EMI Sweep Setup
Amplitude, phase and control voltage were swept; EMI was injected through different ports.
Sweep variables
All-port / multi-port EMI testbench

## Slide 24
Intermediate Architecture: Phase-Dependent Delay
The response remained irregular; this confirmed incomplete common-mode rejection.
Delay vs phase
Expanded phase sweep

## Slide 25
Intermediate Architecture: Falling-Edge Behaviour
Falling edge did not behave symmetrically with rising edge, making delay extraction unreliable.
Falling-edge response
Additional falling-edge result

## Slide 26
Supply and Combined EMI Paths
Supply EMI affected current and threshold; combined EMI produced residual jitter.
Supply EMI testbench
Supply EMI delay
All-port delay response

## Slide 27
Intermediate Architecture: Mathematical Insight
Delay error has multiple sensitivity paths, so only cancelling input common-mode noise is insufficient.
Delta t_d = S_in Delta V_in + S_ref Delta V_ref
+ S_DD Delta V_DD + S_SS Delta V_SS
If sensitivities are unequal: residual jitter remains
Design goal: reduce common-mode terms while preserving delay gain

## Slide 28
Final Design Direction
Compressed differential control around the valid operating point

## Slide 29
Differential Pair DC Study
Direct 0-1.8 V control pushed the pair out of its valid small-signal/saturation region.
Differential pair schematic
DC output mapping

## Slide 30
Compressed Control Mapping
Full rail-to-rail control A is mapped into a small differential swing around 0.9 V.
V_CM = 0.9 V
V_plus = 0.9 + k(A - 0.9)
V_minus = 0.9 - k(A - 0.9)
k ~= 0.15
v_id = 2k(A - 0.9)

## Slide 31
Why Compression Helped
Both differential-pair transistors remain closer to saturation.
Common-mode cancellation assumption becomes more valid.
Low-amplitude EMI appears similarly on both branches.
Trade-off: compressed input reduces control sensitivity.
Compressed/small-signal operation around 0.9 V.

## Slide 32
First Edit: Final Carried-Forward Cadence Direction
This is the actual Cadence-based architecture direction used in the final story. No AI-generated white diagram is used.
First edit schematic
Delay response
EMI testbench/result

## Slide 33
Second Edit: Ruled Out
Single-ended current mirror/tail-control attempt was rejected because delay became nearly constant.
Second edit schematic
Nearly constant delay with sweep

## Slide 34
Final EMI Observations
Low frequency / low amplitude: partial cancellation. High frequency / high amplitude: residual jitter remains.
Frequency and phase sweep
Frequency-dependent jitter
Average delay trend

## Slide 35
Common-Mode Cancellation: Final Equation
Differential cancellation works only if both branches are matched and equally disturbed.
V_plus = V_CM + v_id/2 + v_cm
V_minus = V_CM - v_id/2 + v_cm
V_plus - V_minus = v_id
T_plus = T(V_plus)+delta_cm
T_minus = T(V_minus)+delta_cm
Delta T = T_plus - T_minus

## Slide 36
Small-Signal Delay Path
This is the final analytical link from differential input to delay modulation.
i_o = g_m v_d
v_b = A_v v_d
Delta I = g_m,tail A_v v_d
t_d = C Delta V / (I_0 + Delta I)
Delta t_d ~= -(t_d0/I_0) g_m,tail A_v v_d

## Slide 37
Final BTP Contributions
Documented pre-midsem baseline VTC, PVT and EMI behaviour.
Implemented and analyzed SET-H CDC and input-conditioned cells.
Identified why direct differential architectures failed.
Developed compressed differential control for partial EMI cancellation.
Explained remaining high-frequency limitations using CMRR and parasitics.
Final frequency-dependent residual jitter.

## Slide 38
Final BTP Conclusion
EMI in a VTC becomes phase-dependent timing jitter.
Dual VCDU reduces common PVT variation, but not unequal EMI coupling.
Differential architecture helps only when biasing, matching and small-signal operation are preserved.
The final proposed direction is a Cadence-based compressed differential-control architecture.
Final carried-forward Cadence schematic.